## Slide 1: SAFARI Project & Seminars Courses Exploration of Emerging Memory Systems
Haocong Luo
Prof. Onur Mutlu
ETH Zürich
Fall 2022
11 October 2021

## Slide 2: Meeting 2: Project Ideas
Haocong Luo
Prof. Onur Mutlu
ETH Zürich
Fall 2022
11 October 2021

## Slide 3: Projects
Extending Ramulator with New DRAM Standards
Implementing and Evaluating Hybrid Memory Systems
Statistical Extensions For Calculating RowHammer Bit Flip Probability
Incorporating RowHammer protection mechanisms in Ramulator
Adding Memory Controller-Level Support for In-Memory Computation
Making TL-DRAM/SALP Implementations DRAM Standard Agnostic
Implementing and Evaluating SARP/DARP
Non-volatile Memory Extensions
Implement and Evaluating QoS-aware Scheduling Mechanisms
Implement and Evaluating Self-Learning Scheduling Mechanisms

## Slide 4: Extending Ramulator with New DRAM Standards

## Slide 5: Extending Ramulator with New DRAM Standards
Motivation
  Ramulator supports a wide range of DRAM standards, but some recent DRAM standards are not yet available
Goal
  Extend Ramulator with new DRAM standards (e.g., DDR5, LPDDR5, GDDR6)
Expected results
  Modify the memory controller in Ramulator to support new organization and commands that are part of the new DRAM standards

## Slide 6: Implementing and Evaluating Hybrid Memory Systems

## Slide 7: Implementing and Evaluating Hybrid Memory Systems
Motivation
  Hybrid memory system designs have significant performance and energy efficiency benefits
Goal
  Study existing hybrid memory proposals and implement some of them in Ramulator
  Evaluate the performance and energy efficiency of such design using popular benchmarks
Expected results
  Ramulator with hybrid memory support
  Performance/energy analysis of hybrid memory designs

## Slide 8: Related Papers
Kotra et al., “CHAMELEON: A Dynamically reconfigurable heterogeneous memory system”, in MICRO’ 18.
Prodromou et al., “MemPod: A Clustered Architecture for Efficient and Scalable Migration in Flat Address Space Multi-level Memories”, in HPCA’ 17.
Sim et al., “Transparent Hardware Management of Stacked DRAM As Part of Memory”, in MICRO’ 15.
Agarwal et al., “Thermostat: Application-transparent Page Management for Two-tiered Main Memory”, in ASPLOS’ 17.
Meswani et al., “Heterogeneous memory architectures: A HW/SW approach for mixing die-stacked and off-package memories”, in HPCA’ 15.
Lee et al., “A fully associative, tagless DRAM cache”, in ISCA’ 15.
Vasilakis et al., “Hybrid2: Combining caching and migration in hybrid memory systems”, in HPCA’ 20.
…

## Slide 9: Statistical Extensions to Calculate RowHammer Bit Flip Probability

## Slide 10: Estimating RowHammer Bit Flip Probability
Motivation
  Many factors (e.g., access patterns, data pattern dependence, DRAM cell array architecture) affect RowHammer
  Quickly estimating the RowHammer bit flip probability is important for designing new RowHammer attacks and defenses
Goal
  Extend Ramulator to statistically estimate RowHammer bit flip probability during execution of workloads
Expected results
  Ramulator should report RowHammer bit flip probability along with performance statistics

## Slide 11: Incorporating RowHammer Protection Mechanisms in Ramulator

## Slide 12: RowHammer Protection Mechanisms in Ramulator
Motivation
  Modern DRAM is susceptible to RowHammer
  RowHammer protection mechanisms incur non-negligible performance and energy overheads
Goal
  Implement RowHammer protection mechanisms in Ramulator to evaluate their performance and energy overheads
Expected results
  Support for RowHammer protection mechanisms that can be selectively turned on
  Performance/energy overhead analysis of the implemented RowHammer protection mechanisms

## Slide 13: Related Papers
Kim et al. “Flipping Bits in DRAM without Accessing Them,” in ISCA’ 14.
Seyedzadeh et al., “Counter-based Tree Structure for Row Hammering Mitigation in DRAM”, in CAL’ 17.
Son et al., “Making DRAM Stronger Against Row Hammering,” in DAC’ 17.
You et al., “MRLoc: Mitigating Row-Hammering Based on Memory Locality”, in DAC’ 19.
Lee et al., “TWiCe: Preventing Row-hammering by Exploiting Time Window Counters”, in ISCA’ 19.
Park et al., “Graphene: Strong yet Lightweight Row Hammer Protection”, in MICRO’ 20.
Yaglikci et al., “BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows”, in HPCA’ 21.
Marazzi et al., “ProTRR: Principled yet Optimal In-DRAM Target Row Refresh”, in S&P’ 22.

## Slide 14: Adding Memory Controller-Level Support for In-Memory Computation

## Slide 15: Support for In-Memory Computation
Motivation
  In-memory computing improves execution efficiency by eliminating excessive data movement by moving computation closer to where the data resides
Goal
  Implement easily extensible memory controller-level support for in-memory computation in Ramulator
Expected results
  The memory controller should support simple in-memory operations (e.g., RowClone, Ambit)
  Enabling to easily add new commands for different in-memory operations

## Slide 16: Making TL-DRAM/SALP DRAM Standard Agnostic

## Slide 17: DRAM Standard Agnostic TL-DRAM/SALP
Motivation
  Ramulator currently implements Tiered-Latency DRAM as a separate DRAM standards
  Same for Subarray-level Parallelism (SALP)
Goal
  Re-implement TL-DRAM and SALP in a DRAM standard agnostic way
Expected results
  Ramulator should implement TL-DRAM and SALP as separate mechanisms
  Using TL-DRAM and SALP in combination with different DRAM standards (e.g., DDR4, LPDDR4) should be supported

## Slide 18: Related Papers
Lee et al., "Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture“, in HPCA’ 13.
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM”, in ISCA’ 12.

## Slide 19: Implementing and Evaluating SARP/DARP

## Slide 20: Implementing and Evaluating SARP/DARP
Motivation
  Chang+ [1] show the benefits of parallelizing refreshes with accesses in DRAM
Goal
  Implement SARP and DARP mechanisms in Ramulator
Expected results
  Ramulator extended with SARP/DARP support
  Performance/energy benefits analysis of SARP/DARP using popular benchmark
[1] Chang et al., “Improving DRAM Performance by Parallelizing Refreshes with Accesses”, in HPCA’ 14.

## Slide 21: Related Papers
Chang et al., “Improving DRAM Performance by Parallelizing Refreshes with Accesses”, in HPCA’ 14.

## Slide 22: Non-Volatile Memory Extensions

## Slide 23: Non-Volatile Memory Extensions
Motivation
  Emerging Non-Volatile Memory (NVM) technologies offer better device density with DRAM-like access latencies
Goal
  Extend Ramulator to support popular NVM
Expected results
  Model of the performance and endurance of NVM
  Evaluation of popular benchmarks using the implemented NVM

## Slide 24: Implement and Evaluating QoS-aware Scheduling Mechanisms

## Slide 25: Implement and Evaluating QoS-aware Scheduling Mechanisms
Motivation
  QoS-aware memory request scheduling mechanisms increases overall system performance when dealing with many different workloads with different memory access characteristics
Goal
  Extend Ramulator to support QoS-aware memory scheduling mechanisms
Expected results
  Model and implement QoS-aware memory scheduling mechanism(s).
  Evaluation of the performance of the said mechanism(s).

## Slide 26: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
  Takeaway: Preserving within-thread bank-parallelism improves performance; request batching improves fairness
ATLAS memory scheduler [Kim+ HPCA’10]
  Idea: Prioritize threads that have attained the least service from the memory scheduler
  Takeaway: Prioritizing “light” threads improves performance

## Slide 27: QoS-Aware Memory Scheduling: Evolution
Thread cluster memory scheduling [Kim+ MICRO’10, Top Picks’11]
  Idea: Cluster threads into two groups (latency vs. bandwidth sensitive); prioritize the latency-sensitive ones; employ a fairness policy in the bandwidth sensitive group
  Takeaway: Heterogeneous scheduling policy that is different based on thread behavior maximizes both performance and fairness
Integrated Memory Channel Partitioning and Scheduling [Muralidhara+ MICRO’11]
    Idea: Only prioritize very latency-sensitive threads in the scheduler; mitigate all other applications’ interference via channel partitioning
    Takeaway: Intelligently combining application-aware channel partitioning and memory scheduling provides better performance than either

## Slide 28: QoS-Aware Memory Scheduling: Evolution
Parallel application memory scheduling [Ebrahimi+ MICRO’11]
  Idea: Identify and prioritize limiter threads of a multithreaded application in the memory scheduler; provide fast and fair progress to non-limiter threads
  Takeaway: Carefully prioritizing between limiter and non-limiter threads of a parallel application improves performance
Staged memory scheduling [Ausavarungnirun+ ISCA’12]
    Idea: Divide the functional tasks of an application-aware memory scheduler into multiple distinct stages, where each stage is significantly simpler than a monolithic scheduler
    Takeaway: Staging enables the design of a scalable and relatively simpler application-aware memory scheduler that works on very large request buffers

## Slide 29: QoS-Aware Memory Scheduling: Evolution
MISE: Memory Slowdown Model [Subramanian+ HPCA’13]
    Idea: Estimate the performance of a thread by estimating its change in memory request service rate when run alone vs. shared  use this simple model to estimate slowdown to design a scheduling policy that provides predictable performance or fairness
    Takeaway: Request service rate of a thread is a good proxy for its performance; alone request service rate can be estimated by giving high priority to the thread in memory scheduling for a while
ASM: Application Slowdown Model [Subramanian+ MICRO’15]
  Idea: Extend MISE to take into account cache+memory interference
  Takeaway: Cache access rate of an application can be estimated accurately and is a good proxy for application performance

## Slide 30: QoS-Aware Memory Scheduling: Evolution
BLISS: Blacklisting Memory Scheduler [Subramanian+ ICCD’14, TPDS’16]
  Idea: Deprioritize (i.e., blacklist) a thread that has consecutively serviced a large number of requests
  Takeaway: Blacklisting greatly reduces interference enables the scheduler to be simple without requiring full thread ranking
DASH: Deadline-Aware Memory Scheduler [Usui+ TACO’16]
  Idea: Balance prioritization between CPUs, GPUs and Hardware Accelerators (HWA) by keeping HWA progress in check vs. deadlines such that HWAs do not hog performance and appropriately distinguishing between latency-sensitive vs. bandwidth-sensitive CPU workloads
  Takeaway: Proper control of HWA progress and application-aware CPU prioritization leads to better system performance while meeting HWA deadlines

## Slide 31: QoS-Aware Memory Scheduling: Evolution
Prefetch-aware shared resource management [Ebrahimi+ ISCA’11] [Ebrahimi+ MICRO’09] [Ebrahimi+ HPCA’09] [Lee+ MICRO’08’09]
  Idea: Prioritize prefetches depending on how they affect system performance; even accurate prefetches can degrade performance of the system
  Takeaway: Carefully controlling and prioritizing prefetch requests improves performance and fairness
DRAM-Aware last-level cache policies and write scheduling [Lee+ HPS Tech Report’10] [Seshadri+ ISCA’14]
  Idea: Design cache eviction and replacement policies such that they proactively exploit the state of the memory controller and DRAM (e.g., proactively evict data from the cache that hit in open rows)
  Takeaway: Coordination of last-level cache and DRAM policies improves performance and fairness; writes should not be ignored

## Slide 32: QoS-Aware Memory Scheduling: Evolution
FIRM: Memory Scheduling for NVM [Zhao+ MICRO’14]
  Idea: Carefully handle write-read prioritization with coarse-grained batching and application-aware scheduling
  Takeaway: Carefully controlling and prioritizing write requests improves performance and fairness; write requests are especially critical in NVMs
Criticality-Aware Memory Scheduling for GPUs [Jog+ SIGMETRICS’16]
  Idea: Prioritize latency-critical cores’ requests in a GPU system
  Takeaway: Need to carefully balance locality and criticality to make sure performance improves by taking advantage of both
Worst-case Execution Time Based Memory Scheduling for Real-Time Systems [Kim+ RTAS’14, JRTS’16]

## Slide 33: Implement and Evaluating Self-Learning Scheduling Mechanisms

## Slide 34: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 35: Projects
Extending Ramulator with New DRAM Standards
Implementing and Evaluating Hybrid Memory Systems
Statistical Extensions For Calculating RowHammer Bit Flip Probability
Incorporating RowHammer protection mechanisms in Ramulator
Adding Memory Controller-Level Support for In-Memory Computation
Making TL-DRAM/SALP Implementations DRAM Standard Agnostic
Implementing and Evaluating SARP/DARP
Non-volatile Memory Extensions
Implement and Evaluating QoS-aware Scheduling Mechanisms
Implement and Evaluating Self-Learning Scheduling Mechanisms

## Slide 36: SAFARI Project & Seminars Courses Exploration of Emerging Memory Systems
Haocong Luo
Prof. Onur Mutlu
ETH Zürich
Fall 2022
11 October 2021